## Slide 1
Review: Idea of The TTL-based Buffer Management Scheme
Switch Model for Implementing The TTL-based Buffer Management Scheme
    Proof: The TTL-based Buffer Management Scheme is Deadlock-free.
Outline

## Slide 2
Review: Idea of The TTL-based Buffer Management Scheme
Switch Model for Implementing The TTL-based Buffer Management Scheme
    Proof: The TTL-based Buffer Management Scheme is Deadlock-free.
Outline

## Slide 3: TTL-based Buffer Management Scheme
Class n
…
Class k
…
Class 2
Class 1
Class n
…
Class k +1
…
Class 2
Class 1
Key idea of TTL-based buffer management scheme (BMS):
Divide switch buffer into n partitions of n priority classes.
Assign a priority to a packet based on the TTL value of the packet at each hop. TTL value of a packet will decrease by 1 per hop. We increase the priority of a packet by 1 per hop, correspondingly.
Switch buffer
Switch buffer
Switch at hop k
Switch at hop k+1
packet

## Slide 4
Review: Idea of The TTL-based Buffer Management Scheme
Switch Model for Implementing The TTL-based Buffer Management Scheme
    Proof: The TTL-based Buffer Management Scheme is Deadlock-free.
Outline

## Slide 5
The switch model consists of five elements: switch port, forwarding engine, PFC engine, crossbar and switch buffer.
Switch Model

## Slide 6
Each switch port consists of an input port and an output port, and is connected with a link.
Switch Model

## Slide 7
Forwarding engine is the element to make routing and/or switching decisions.
Switch Model

## Slide 8
PFC engine is the element to perform PFC function.
Switch Model

## Slide 9
Switch buffer is used to buffer incoming packets. We assume shared buffer in our model.
Switch Model

## Slide 10
We use virtual ingress queue (VIQ) to track the incoming packets. Each VIQ is uniquely corresponding to an input port.
Switch Model

## Slide 11
We use virtual egress queue (VEQ) to track the outgoing packets. Each VEQ is uniquely corresponding to an output port.
Switch Model

## Slide 12
both VIQ and VEQ consist of k queues, with each queue corresponding to a priority class. A packet of priority class j will enter the j-th queue of its destined VIQ and VEQ.
Switch Model

## Slide 13
In the following slides, we use to denote the j-th queue of VIQ i, and to denote the j-th queue of VEQ i (1 ≤ i ≤ n, 1 ≤ j ≤ k).
Switch Model

## Slide 14
It is not necessary for our switch model to have both ingress buffer and egress buffer at the same time. It depends on the buffering strategy.
Discussion of Buffering Strategy

## Slide 15
It is not necessary for our switch model to have both ingress buffer and egress buffer at the same time. It depends on the buffering strategy.
  output-queued strategy: there will be no ingress buffer. VIQs are simply some counters to record the bytes of buffered packets received by different input ports.
  Input-queued strategy: there will be no egress buffer. VEQs can be simulated using virtual output queuing technique at the ingress buffer.
  Combined-input-and-output-queued strategy: the switch will have both ingress buffer and egress buffer.
Discussion of Buffering Strategy

## Slide 16
Crossbar is the element to switch packet cells from the ingress buffer to the egress buffer.
Switch Model

## Slide 17
The function of the PFC mechanism consists of four parts, as shown in the figure.
Modified PFC Mechanism

## Slide 18
Main difference: if the queue length of some queue exceeds the PFC threshold, PFC engine will pause priority class j-1 of the incoming link instead of priority class j.
Modified PFC Mechanism

## Slide 19
Buffer Division: we divide the buffer of network nodes into k partitions, and let the j-th partition associated with priority class j. If a packet is classified into priority class j, it will be buffered in the j-th buffer partition.
TTL-based BMS under The Switch Model

## Slide 20
Buffer Division: we divide the buffer of network nodes into k partitions, and let the j-th partition associated with priority class j. If a packet is classified into priority class j, it will be buffered in the j-th buffer partition.
TTL-based BMS under The Switch Model
TTL-based Packet Buffering:
  Initially, we set TTL values of all the packets to ttl0 = d at all the source servers, where d is the number of hops of the longest path in the network.
  Let ttli be the TTL value of a packet p at its i-th hop (i ≥ 0). At every hop, the priority class of any incoming packet p is calculated as λp = ttl0 − ttli.

## Slide 21
Review: Idea of The TTL-based Buffer Management Scheme
Switch Model for Implementing The TTL-based Buffer Management Scheme
    Proof: The TTL-based Buffer Management Scheme is Deadlock-free.
Outline

## Slide 22
High Level Idea: For arbitrary given time t, to show the network is not in a state of deadlock, we can stop the injection of new packets into the network, and prove that all the packets remaining in the network can be drained within some finite time.
Proof of Deadlock-free

## Slide 23
First, we consider the queues of priority class k. These queues are of highest priority and thus will not be paused by PFC PAUSE messages. So packets in these queues can be drained within some finite time.
Proof of Deadlock-free

## Slide 24
Packets in the queues of priority class k-1 will not be permanently paused as the packets in the queues of priority class k will be drained within some finite time. Therefore, packets in the queues of priority class k-1 can also be drained with some finite time.
Proof of Deadlock-free

## Slide 25
Recursively, we can prove that packets in all the queues can be drained within some finite some.
Proof of Deadlock-free