## Slide 1
Reducing The Number Of Priorities Needed By TTL-based Solution
  Per Port Per Priority PFC Headroom + Fixed TTL-to-priority Mapping
  Per Port Per Priority PFC Headroom + Flexible TTL-to-priority Mapping
Outline

## Slide 2
Reducing The Number Of Priorities Needed By TTL-based Solution
  Per Port Per Priority PFC Headroom + Fixed TTL-to-priority Mapping
  Per Port Per Priority PFC Headroom + Flexible TTL-to-priority Mapping
Outline

## Slide 3
…
…
…
…
TTL = ttl0-2k
TTL = ttl0-1
TTL = ttl0-3-2k
Assuming at all source servers, initial TTL value of all packets are set to ttl0 (a even number).
Reducing Number of Priorities Needed By Using Per Port Per Priority PFC Headroom Reservation

## Slide 4
…
…
…
…
TTL = ttl0-2k
TTL = ttl0-1
TTL = ttl0-3-2k
Assuming at all source servers, initial TTL value of all packets are set to ttl0 (a even number).
TTL = ttl0-2-2k
TTL = ttl0-4-2k
Reducing Number of Priorities Needed By Using Per Port Per Priority PFC Headroom Reservation

## Slide 5
…
…
…
…
TTL = ttl0-2k
TTL = ttl0-1
TTL = ttl0-3-2k
TTL = ttl0-3-2k
Assuming at all source servers, initial TTL value of all packets are set to ttl0 (a even number).
TTL = ttl0-2-2k
TTL = ttl0-4-2k
Reducing Number of Priorities Needed By Using Per Port Per Priority PFC Headroom Reservation

## Slide 6
…
…
…
…
Down-Up Bounce: if a packet received from an upper level switch is forwarded to some upper level switch, we call it a down-up bounce.
Reducing Number of Priorities Needed By Using Per Port Per Priority PFC Headroom Reservation
Definition of down-up bounce:

## Slide 7
Reducing Number of Priorities Needed By Using Per Port Per Priority PFC Headroom Reservation
…
…
…
…
Case 1: down-up bounce is not part of any normal path. In this case, only shortest path routing is expected. We can set ttl0 = 7.
path 1
path 2

## Slide 8
…
…
…
…
TTL = 7, 5, 3, 1
TTL = 6
TTL = 4, 2
TTL = 4, 2
In this case, 3 priorities will be needed.
TTL = 5, 3, 1
TTL = 3, 1
Reducing Number of Priorities Needed By Using Per Port Per Priority PFC Headroom Reservation

## Slide 9
…
…
…
…
TTL = 7, 5, 3, 1
TTL = 6
TTL = 4, 2
TTL = 4, 2
We can simply drop those packets that cannot reach destination before their TTL is reduced to 0.
TTL = 5, 3, 1
TTL = 3, 1
Reducing Number of Priorities Needed By Using Per Port Per Priority PFC Headroom Reservation

## Slide 10
…
…
…
…
TTL = 7, 5, 3, 1
TTL = 6
TTL = 4, 2
TTL = 4
So for case 1, the number of priorities needed is 2. Total PFC headroom is 1.5bhr*n=5.76MB for Arista 7050QX32 switch when Scell = 208bytes.
TTL = 5, 3
TTL = 3
Reducing Number of Priorities Needed By Using Per Port Per Priority PFC Headroom Reservation

## Slide 11
Reducing Number of Priorities Needed By Using Per Port Per Priority PFC Headroom Reservation
…
…
…
…
Case 2: down-up bounce is expected to occur m times in a normal path. In this case, we can set ttl0 = 7+2m.
Path with 2 down-up bounces.

## Slide 12
…
…
…
…
TTL = (7, 5, 3, 1)
+ 2k
TTL = 6+2m
TTL = (4, 2)+2k
TTL = 4 + 2k
The number of priorities needed is 2+m. Total PFC headroom is (1.5+m) bhr*n.
TTL = (5, 3)+2k
TTL = 3+2k
Reducing Number of Priorities Needed By Using Per Port Per Priority PFC Headroom Reservation
(0 <= k <= m)

## Slide 13
Reducing The Number Of Priorities Needed By TTL-based Solution
  Per Port Per Priority PFC Headroom + Fixed TTL-to-priority Mapping
  Per Port Per Priority PFC Headroom + Flexible TTL-to-priority Mapping
Outline

## Slide 14
…
…
…
…
TTL = 7, 5, 3, 1
TTL = 6
TTL = 4, 2
TTL = 4
In case 1, 2 priorities are needed because normal shortest path and abnormal path with down-up bounce cannot be differentiated.
TTL = 5, 3
TTL = 3
Reducing Number of Priorities Needed By Using Flexible TTL-to-Priority Mapping
normal shortest path
abnormal path

## Slide 15
…
…
…
…
TTL = 7, 5, 3, 1
TTL = 6
TTL = 4, 2
TTL = 4
We can differentiate normal and abnormal paths by using a combination of (ingress port, egress port, TTL).
TTL = 5, 3
TTL = 3
Reducing Number of Priorities Needed By Using Flexible TTL-to-Priority Mapping
normal shortest path
abnormal path

## Slide 16
…
…
…
…
TTL = 7, 5, 3, 1
TTL = 6
TTL = 4, 2
TTL = 4
Packets of abnormal packets can be dropped or mapped to a lossy priority. So the number of lossless priorities is reduced to 1 for case 1.
TTL = 5, 3
TTL = 3
Reducing Number of Priorities Needed By Using Flexible TTL-to-Priority Mapping

## Slide 17
…
…
…
…
Previously we have proven that if we increase the priority of a packet when it meets a down-up bounce, there will be no deadlock.
Priority 1
Priority 2
Priority 3
Reducing Number of Priorities Needed By Using Flexible TTL-to-Priority Mapping

## Slide 18
…
…
…
…
The idea of the proof is to show that the packets of highest priority currently buffered in the lowest-level switch will not be paused.
Priority 1
Priority 2
Priority 3
Reducing Number of Priorities Needed By Using Flexible TTL-to-Priority Mapping

## Slide 19
…
…
…
…
condition to increase priority: UP ingress port + UP egress port + valid TTL + non-highest priority). The number of lossless priorities is reduced to m+1 for case 2.
Priority 1
Priority 2
Priority 3
Reducing Number of Priorities Needed By Using Flexible TTL-to-Priority Mapping

## Slide 20
TOR2
…
…
…
…
If 1 down-up bounce is allowed in normal paths, switch TOR2 cannot differentiate normal path and abnormal path. So m+1 =2 lossless priorities are necessary to ensure deadlock-free.
Priority 1
Priority 2
Reducing Number of Priorities Needed By Using Flexible TTL-to-Priority Mapping
Abnormal path: includes a loop.

## Slide 21
TOR2
…
…
…
…
If 1 down-up bounce is allowed in normal paths, switch TOR2 cannot differentiate normal path and abnormal path. So m+1 =2 lossless priorities are necessary to ensure deadlock-free.
Priority 1
Priority 2
Reducing Number of Priorities Needed By Using Flexible TTL-to-Priority Mapping
Normal path: 1 down-up bounce is included.