## Slide 1
Review: TTL-based Solution
Problems Caused by The TTL-based Solution
  PFC Headroom is Too Large
  Per Flow Fairness Will be Violated
Outline

## Slide 2
Review: TTL-based Solution
Problems Caused by The TTL-based Solution
  PFC Headroom is Too Large
  Per Flow Fairness Will be Violated
Outline

## Slide 3
Routing induced deadlock
  Routing function includes cyclic buffer dependency.
  Solution: deadlock-free routing algorithm.
Reconfiguration induced deadlock
      Cyclic buffer dependency is created during routing reconfiguration.
      Solution: deadlock-free routing reconfiguration.
Failure induced deadlock
  Routing protocols like BGP can have transient loop under failures which may cause deadlock.
  Solution: deadlock-free BGP.
Bug or misconfiguration induced deadlock.
  Solution: fix the bug or misconfiguration.
Review: A Solution for All Kinds of Deadlocks
It is more desired to have a single solution for handling all the deadlocks.

## Slide 4: Review: Key idea of TTL-base Solution
Class n
…
Class k
…
Class 2
Class 1
Class n
…
Class k +1
…
Class 2
Class 1
Divide switch buffer into n partitions of n priority classes.
Assign a priority to a packet based on the TTL value of the packet at each hop. TTL value of a packet will decrease by 1 per hop. We increase the priority of a packet by 1 per hop, correspondingly.
Switch buffer
Switch buffer
Switch at hop k
Switch at hop k+1
packet

## Slide 5: Review: Key idea of TTL-base Solution
TTL-based solution can prevent all kinds of deadlock as it can eliminate cyclic buffer dependency.
Topology and flows
Cyclic buffer dependency without BMS.
Cyclic buffer dependency without BMS.

## Slide 6
The switch model consists of five elements: switch port, forwarding engine, PFC engine, crossbar and switch buffer.
Review: Switch Model

## Slide 7
Buffer Division:
  Divide switch buffer into k partitions, and let the j-th partition associated with priority class j.
  If a packet is classified into priority class j, it will be buffered in the j-th buffer partition.
Review: TTL-based Solution
TTL-based Packet Buffering:
  Initially, we set TTL values of all the packets to ttl0 = d at all the source servers, where d is the number of hops of the longest path in the network.
  Let ttli be the TTL value of a packet p at its i-th hop (i ≥ 0). At every hop, the priority class of any incoming packet p is calculated as λp = ttl0 − ttli.

## Slide 8: Dedicated Buffer for Different Priorities Is Necessary
If we do not reserve dedicated buffer for every priority class, there can still be deadlock.
Topology and flows
No cyclic dependency among priority queues
Cyclic buffer waiting

## Slide 9
Alternative Buffer Division:
  divide the switch buffer into k+1 partitions. The first k partitions are dedicated for the k priority classes. The k+1 partition is shared by all the priority classes.
  During runtime, a packet of priority class j will always use its dedicated buffer before use the shared buffer.
Review: Alternative Way To Do Buffer Division

## Slide 10
Review: TTL-based Solution
Problems Caused by The TTL-based Solution
  PFC Headroom is Too Large
  Per Flow Fairness Will be Violated
Outline

## Slide 11
Calculation of PFC Headroom
Let t1 be the time a receiver decides to stop the data transmission of an immediate upstream device.
Let t2 be the time the sender has stopped the data transmission and there are no bytes of packets remaining on the wire.
PFC headroom is the size of buffer the receiver must reserve to accommodate the packets it may receive during [t1, t2].
Sender
Receiver
data packet from sender to receiver
PFC message
data packet from receiver to sender
Buffer

## Slide 12
Calculation of PFC Headroom
Notations:
sMTU | Value of maximum transmission unit (typically 1500bytes).
Smin | Value of minimum transmission unit (typically 64bytes).
SPFC | Size of PFC control message.
Scell | Size of buffer cell.
Sp | Size of packet p.
rl | Line rate of network links.

## Slide 13
Calculation of PFC Headroom
1. Buffer headroom for buffering packets already on the wire right before the receiver decides to send a PAUSE message (denoted as twire): twire is the propagation delay of the network link.
Sender
Receiver
Buffer
Bytes of packets on the wire: rl*twire
Needed buffer headroom: rl*twire*

## Slide 14
Calculation of PFC Headroom
2. Buffer headroom for buffering packets sent by the sender during the period the receiver sends out a PAUSE message (denoted as tsnd):
Sender
Receiver
duration of period: tsnd= (sMTU + sPFC)/rl
Bytes of packets the sender can send: rl*tsnd
Needed buffer headroom: rl*tsnd*
Buffer

## Slide 15
Calculation of PFC Headroom
3. Buffer headroom for buffering packets sent by the sender during the period when the PAUSE message propagates from the receiver to the sender (denoted as twire):
Sender
Receiver
Buffer
duration of period: twire
Bytes of packets the sender can send: rl*twire
Needed buffer headroom: rl*twire*

## Slide 16
Calculation of PFC Headroom
4. Buffer headroom for buffering packets sent by the sender during the period the sender to receive the PAUSE message. (denoted as trev).
duration of period: trev= sPFC/rl
Bytes of packets the sender can send: rl*trev
Needed buffer headroom: rl*trev*
Sender
Receiver
Buffer

## Slide 17
Calculation of PFC Headroom
5. Buffer headroom for buffering packets sent by the sender during the period the sender processes the PAUSE message (denoted as tpro):
duration of period: tpro
Bytes of packets the sender can send: rl*tpro
Needed buffer headroom: rl*tpro*
Sender
Receiver
Buffer

## Slide 18
Calculation of PFC Headroom
6. Buffer headroom for buffering packets sent by the sender during the period the sender stops packet transmission (denoted as tstop):
duration of period: tstop=sMTU/rl
Bytes of packets the sender can send: rl*tstop=sMTU
Needed buffer headroom:
Sender
Receiver
Buffer

## Slide 19
Calculation of PFC Headroom
In summary, the per port per priority PFC headroom bhr can be expressed using the following equation:
bhr = (sMTU +2sPFC +rl (2twire+tpro))+

## Slide 20
Typical Values of Variables In The Equation
For typical TCP/IP based RDMA DCNs, we have sMTU = 1500bytes, smin = 64bytes, sPFC = 64bytes.
For Broadcom chipset, we have scell=208bytes.
Every 100 meters of link delays the reception of a packet by about 500ns for copper cables. The length of links used in a single DCN is usually no larger than 300 meters. Hence we have twire ≤ 1.5us.
According to the data from Chuanxiong, we have tpro ≤ 4us.

## Slide 21
Calculation of PFC Headroom
In summary, the per port per priority PFC headroom bhr can be expressed using the following equation:
bhr = (sMTU +2sPFC +rl (2twire+tpro))+
= 120705bytes 120KB (when rl = 40Gbps)
For commodity switches like Arista 7050QX32 which has 32 full duplex 40Gbps ports, when supporting 8 priority classes, it requires about 32 ∗ 8 ∗ 120 = 30MB buffer as the PFC headroom, which is larger than the 12MB switch buffer.

## Slide 22
If = 64bytes:
bhr = (sMTU +2sPFC +rl (2twire+tpro))+
= 73665bytes 74KB (when rl = 40Gbps)
For commodity switches like Arista 7050QX32 which has 32 full duplex 40Gbps ports, when supporting 8 priority classes, it requires about 32 ∗ 8 ∗ 74 = 18.5MB buffer as the PFC headroom, which is larger than the 12MB switch buffer.
Using Smaller Buffer Cell Can Help
= 64bytes, sp=65bytes

## Slide 23
If = 16bytes:
bhr = (sMTU +2sPFC +rl (2twire+tpro))+
= 46581bytes 47KB (when rl = 40Gbps)
For commodity switches like Arista 7050QX32 which has 32 full duplex 40Gbps ports, when supporting 8 priority classes, it requires about 32 ∗ 8 ∗ 47 = 11.75MB buffer as the PFC headroom, which is larger than the 12MB switch buffer.
Using Smaller Buffer Cell Can Help
= 16bytes, sp=65bytes

## Slide 24
If = 208bytes:
bhr = (sMTU +2sPFC +rl (2twire+tpro))+
= 74405bytes 75KB (when rl = 40Gbps)
For commodity switches like Arista 7050QX32 which has 32 full duplex 40Gbps ports, when supporting 8 priority classes, it requires about 32 ∗ 8 ∗ 75 = 18.75MB buffer as the PFC headroom, which is larger than the 12MB switch buffer.
Increasing The Size of Minimum Packet Can Help
= 208bytes, sp=209bytes

## Slide 25
Reducing Number of Priorities Needed by The TTL-based Solution
…
…
…
…
Assuming at all source servers, initial TTL value of all packets are set to ttl0 (a even number).

## Slide 26
Reducing Number of Priorities Needed by The TTL-based Solution
…
…
…
…
TTL = ttl0-2k
TTL = ttl0-1-2k
TTL = ttl0-2-2k
TTL = ttl0-3-2k
Assuming at all source servers, initial TTL value of all packets are set to ttl0 (a even number).

## Slide 27
Reducing Number of Priorities Needed by The TTL-based Solution
…
…
…
…
Observation: switches at the same layer only need to support either all the even priority or all the odd priority.
TTL = ttl0-2k
TTL = ttl0-1-2k
TTL = ttl0-2-2k
TTL = ttl0-3-2k

## Slide 28
Reducing Number of Priorities Needed by The TTL-based Solution
…
…
…
…
Priority: 0 2 4 6 8
Priority: 1 3 5 7
Priority: 2 4 6
Priority: 1 3 5
For Arista 7050QX32 switch, the PFC headroom can be reduced to a half. When Scell = 208bytes, bhr =15MB. When Scell = 16bytes, bhr =5.875MB.

## Slide 29
Review: TTL-based Solution
Problems Caused by The TTL-based Solution
  PFC Headroom is Too Large
  Per Flow Fairness Will be Violated
Outline

## Slide 30
Per Flow Fairness Under TTL-based Solution
…
…
…
…
H1
H2
H3
H4
B
We consider three flows f1, f2 and f3 from hosts H2, H3 and H4 to H1, respectively.
f1
f2
f3

## Slide 31
Per Flow Fairness Under TTL-based Solution
…
…
…
…
H1
H2
H3
H4
B
Without applying the TTL-based solution, there is only one queue. Ideally, each flow should share 1/3 bandwidth at the bottleneck link.
f1
f2
f3
rf1:rf2:rf3=::
f3
f1
f2

## Slide 32
Per Flow Fairness Under TTL-based Solution
…
…
…
…
H1
H2
H3
H4
B
With the TTL-based solution, f1 and f2 will share a common queue, while f3 will enter a different queue. This introduces flow unfairness among three flows.
f1
f2
f3
rf1:rf2:rf3=::
f3
f1
f2
Wq1:Wq2=1:1

## Slide 33
Per Flow Fairness Under TTL-based Solution
…
…
…
…
H1
H2
H3
H4
B
We can reserve per flow fairness by dynamically change the weight of different queues. This requires the switch to maintain per flow state, which is too expensive.
f1
f2
f3
rf1:rf2:rf3=::
f3
f1
f2
Wq1:Wq2=2:1